## Slide 13
Notice here that expression for DFF is created using excitation table (AND NOT Truth Table)
D2 = ~C0.C2 + C2~C1 + ~C2C1C0
D1 = m(1,2,5,6) = C1~C0 + ~C1C0 = C0^C1
D0 = m(0,2,4,6) = ~C0

## Slide 18
For Behavioral – always is compulsory
For Data Flow Model – assign is compulsory

## Slide 138
While running the simulation the time to write memory is very high, back door access gives very quick access to the memory during the simulation.
It is copying the data image to the memory. Note however that it is not a real world concept.

## Slide 142: Handshaking using valid and ready
Valid and ready combinations
  Valid = 1, ready = 0  TB is giving valid transaction to memory, but memory is not ready to respond.
  Valid = 0, ready = 1  TB is not giving a valid transaction to memory, but memory is ready to respond.
  Valid = 0, ready = 0  TB is not giving a valid transaction to memory, memory is also not ready to respond.
  Valid = 1, ready = 1  Giving a valid transaction to memory, it is also ready to respond
Handshaking is initiated to say that, I want to give some information to you, other component conveys its readiness by driving ready = 1

## Slide 154
When to declare reg or wire ?
Look for always and initial
List down all the variables used in the statements in the LHS
All those variables should be ‘reg’, any other variables in the code, must be ‘wire’.

## Slide 190
Notice how assigning all positions of vectors is different for x/z and 1. That is replications works for x and z when defined as ‘bz and ‘bx but not for ‘b1.

## Slide 194
This is important. See how y is assigned value using assign. This however is not possible with if-else

## Slide 204
Fork-Join is non-synthesizable
If we want concurrent execution nature inside procedural block, then only option is fork join

## Slide 206
This is very Important

## Slide 207
This is very Important

## Slide 208
This is very Important

## Slide 210
This is very Important

## Slide 219
assign a = if (b) c else d; // Not allowed
assign a = sum(b,c); // Not allowed
assign {co, s} = a+b+ci; //allowed
  // LHS is concatenation of scalar and vector of nets. LHS cannot be reg
assign {a, b} = {c,d,e,f}; // allowed
Implement a 4X1 mux using assign ?
This is done using 2, 2X1 MUXes
assign out = S1 ? (S0 ? i3 : i2) : (S0 ? i1: i0);
I/p S0 S1 O/p
i0 0 0 i0
i1 0 1 i1
i2 1 0 i2
i3 1 1 i3
Similarly 8x1 Mux is
assign out = S2 ? (S1 ? (S0 ? i7 : i6) : (S0 ? i5: i4)) : (S1 ? (S0 ? i3 : i2) : (S0 ? i1: i0));

## Slide 225
bufif1 (buffer if en=1). Tri-State buffers
notif0 and notif1 means output is inversed except same as bufif

## Slide 228
assign statement is used to implement only combinational logic
always statement is used to implement combinational and sequential logic both

## Slide 236
This is very important

## Slide 237
This is very important
Synthesis means converting code to gate level synthesis.
Synthesis tools will do this conversion

## Slide 238
This is very important

## Slide 239
This is very important

## Slide 242
// Ibrahim's Code
module dff (d, clk, res, q);
input d, clk, res;
output reg q;
always @ (posedge clk)
if (res == 1) q = 0;
else q = d;
endmodule
module sample (a, b, c, clk, res, y, w);
input a, b, c, res, clk;
output y, w;
wire n1, n2;
and u1 (n1, a, b);
not u2 (n2, c);
dff d1 (.d(n1), .clk(clk), .res(res), .q(y));
dff d2 (.d(n2), .clk(clk), .res(res), .q(w));
endmodule
// Sreenivasan's Code
module sample (a, b, c, clk, res, y, w);
input a, b, c, res, clk;
output reg y, w;
wire n1, n2;
always @(posedge clk) begin
if (rst == 1) begin
y = 0;
w = 0;
end
else begin
y = a & b;
w = ~c;
end
end
endmodule

## Slide 252
This is very important, Q1, Q2, Q3 will hold just one value at the end of blocking statements hence just ONE D-FF will be inferred as for holding one value only one FF is required

## Slide 253
Q1, Q2, Q3 will be holding 3 different values

## Slide 262
We can use blocking statements inside the always block if there are no dependencies between the statements
Here x,y,z has no dependencies hence blocking statements can be used.

## Slide 263
Why can’t we use non-blocking statements for combinational logic ?
Non-blocking statements uses old values (and not the updated values) hence it is not used in combinational logic
Combinational logics are continuously driven hence as soon as one input changes, output needs to be updated.

## Slide 272
module mux8x1 (i0, i1, i2, i3, i4, i5, i6, i7, sel, y);
always @ (*) begin
if (sel == 3'b000) y = i0;
else if (sel = 3'b001) y = i1;
else if (sel = 3'b010) y = i2;
else if (sel = 3'b011) y = i3;
else if (sel = 3'b100) y = i4;
else if (sel = 3'b101) y = i5;
else if (sel = 3'b110) y = i6;
else if (sel = 3'b111) y = i7;
else y = 1'bx;
end
endmodule
module mux8x1 (i0, i1, i2, i3, i4, i5, i6, i7, sel, y);
always @ (*) begin
case (sel)
3'b000 : y = i0;
3'b001 : y = i1;
3'b010 : y = i2;
3'b011 : y = i3;
3'b100 : y = i4;
3'b101 : y = i5;
3'b110 : y = i6;
3'b111 : y = i7;
default : y = 1'bx;
endcase
end
endmodule

## Slide 277
Very Important

## Slide 315
This is very important. Shows the significance of time precision

## Slide 318
This is very important.
At 8ns a is getting updated hence simulation will enter the always block.
Also notice that a is changing(sensitivity list) before getting assigned to b but b will not be change as simulation is not entering always block before current simulation gets completed and hence b will not change
Value of a is captured 10ns agao but is assigned to b after 10ns

## Slide 319
This is very important.
The value of a is captured after 10ns delay and assigned to b whatever is the current value of a

## Slide 321
$itor – Integer to Real
$ator – Ascii to Real

## Slide 326
%m prints hierarchy and value both. %d, %f both prints value only

## Slide 353
$value$plusargs is elaboration time argument. We used to pass value in vsim that is during elaboration time

## Slide 366
primitive mux2x1(y, i1, i0, sel);
  input i1, i0, sel;
  output y;
  table
    //inputs : outputs;
    //i1 i0 sel y
    ? 0 0 : 0;
    ? 1 0 : 1;
    0 ? 1 : 0;
    1 ? 1 : 1;
  endtable
endprimitive