## Slide 1: APB PROTOCOL
Name: G. Vamsi Girish
M.Tech: NIT Trichy VLSI Systems

## Slide 2: Content
AMBA Bus Architecture.
APB Interface Diagram.
Operation Of APB.
PIN Description.
Master Simulation Result.
APB Interface Diagram with two slaves.
Summary of APB Protocol.

## Slide 3: AMBA ARCHITECTURE

## Slide 4: Interface Diagram
Dummy Signals
READ_WRITE
PRESETn
PCLK
PWRITE
transfer
PREADY
PSEL1
PENABLE

## Slide 5: Operation of APB
IDLE
SETUP
ACCESS/ENABLE

## Slide 6: PIN Description
SIGNAL | SOURCE | Description | WIDTH(Bit)
Transfer | System Bus | APB enable signal. If high APB is activated else APB is disabled | 1
PCLK | Clock Source | All APB functionality occurs at rising edge. | 1
PRESETn | System Bus | An active low signal. | 1
PADDR | APB bridge | The APB address bus can be up to 32 bits. | 8
PSEL1 | APB bridge | There is a PSEL for each slave. It’s an active high signal. | 1
PENABLE | APB bridge | It indicates the 2nd cycle of a data transfer. It’s an active high signal. | 1
PWRITE | APB bridge | Indicates the data transfer direction. PWRITE=1 indicates APB write access(Master to slave) PWRITE=0 indicates APB read access(Slave to master) | 1
PREADY | Slave Interface | This is an input from Slave. It is used to enter access state. | 1
PSLVERR | Slave Interface | This indicates a transfer failure by the slave. | 1
PRDATA | Slave Interface | Read Data. The selected slave drives this bus during read operation | 8
PWDATA | Slave Interface | Write data. This bus is driven by the peripheral bus bridge unit during write cycles when PWRITE is high. | 8

## Slide 7
Write transfers
• With no wait states
• With wait states
With no wait states
At T0 phase all are in initial state and slave as selscted.
The Setup phase of the write transfer occurs at T1 phase. The select signal, PSEL, is asserted, which means that PADDR, PWRITE, and PWDATA must be valid.
The Access phase of the write transfer is shown at T2 where PENABLE is asserted. PREADY is asserted by the Completer at the rising edge of PCLK to indicate that the write data will be accepted at T3. PADDR, PWDATA, and any other control signals, must be stable until the transfer completes. At the end of the transfer, PENABLE is de_asserted. PSEL is also de_asserted, unless there is another transfer to the same peripheral.
Clocking gating : using this clocking method in enable and slave select having one clock pulse delay.

## Slide 8
During an Access phase, when PENABLE is HIGH, the Completer extends the transfer by driving PREADY LOW. The following signals remain unchanged while PREADY remains LOW: • Address signal, PADDR • Direction signal, PWRITE • Select signal, PSELx • Enable signal, PENABLE • Write data signal, PWDATA • Write strobe signal, PSTRB • Protection type signal, PPROT • User request attribute, PAUSER • User write data attribute, PWUSER PREADY can take any value when PENABLE is LOW. This ensures that peripherals that have a fixed two cycle access can tie PREADY HIGH.
With wait states

## Slide 9
Read transfers
Two types of read transfer are described in this section:
• With no wait states.
• With wait states
All signals shown in this section are sampled at the rising edge of PCL
With no wait states

## Slide 10
The transfer is extended if PREADY is driven LOW during an Access phase. The following signals remain unchanged while PREADY remains LOW: • Address signal, PADDR • Direction signal, PWRITE • Select signal, PSEL • Enable signal, PENABLE • Protection signal, PPRO
With wait states
With wait states

## Slide 11
Error response
Error response comes when data read or write not happen properly.
Throughout access phase data address select line should not change.

## Slide 12: Master Write Operation
IDLE State
SETUP State
ENABLE State
IDLE State
SETUP State
ENABLE State
Write with wait state
Write without wait state
Input Signals
Output Signals

## Slide 13: Master Read Operation
Input Signals
Output Signals
IDLE State
SETUP
State
ENABLE
State
IDLE State
SETUP State
ENABLE State
Read with wait state
Read without wait state

## Slide 14
APB2
APB2
APB Master
APB Interface with Slaves

## Slide 15: Read-Write Operation – Slave 1
Read
Operation
Write
Operation

## Slide 16: Read-Write Operation – Slave 2
Read
Operation
Write
Operation

## Slide 17: Summary
Advantages:
Easy to implement.
Low power consumption and area also very less.
Disadvantages: 1.APB having very less bandwidth and throughput.
2. Used for Lower-level modules only.
3. APB protocol not accepted Pipelining concept.